## Slide 1: EFCL Workshop A RISC-V Vector-Processor for High-Throughput Multidimensional Sensor Data Processing
Matteo Perotti mperotti@iis.ee.ethz.ch
17.08.2023

## Slide 2: The curious case of Vector Processors
SUPERCOMPUTER FUGAKU
500 PFLOPS
Second fastest supercomputer in 2023!
Cray X1
256 MFLOPS
Fastest supercomputer in 1976!
Inexpensive silicon
ILP, OoO, Super Scalar
Hype for Vector Processors
End of Dennard’s Scaling
Power wall

## Slide 3: Single-Instruction, Multiple-Data (SIMD) processor
I MEM
D MEM
SIMD
RF
I MEM
D MEM
Scalar
RF
SCALAR CORE
One instruction – One Operation
  BW and Power on the I-MEM
RF size is usually fixed
  One data element per entry
  Too small for highly-intensive WL
    BW and Power on the D-MEM
SIMD CORE
One instruction – Multiple operations
  Lower BW and Power on the I-MEM
RF size is larger
  Multiple data elements per entry
  Better buffering, exploit locality
    Lower BW and Power on the D-MEM
ADD
1 ADD
ADD
N ADD

## Slide 4: Vector Processors – A flexible and efficient choice
I MEM
D MEM
SIMD
RF
ADD
N ADD
I MEM
D MEM
VEC
VRF
ADD
N ADD
SIMD CORE
Vector Length (VL) encoded in the instruction!
  Support new VL? Extend the ISA!
    e.g., add128, add256, ...
  RF is not flexible
VECTOR CORE
Programmable VL
  VRF size decoupled from DP width

## Slide 5: Only Fugaku?
Intel
  From SSE to AVX
Arm
  From NEON to SVE (powering FUGAKU), SVE2, Helium
RISC-V
  V extension
[1] Fugaku supercomputer at SC19. FUJITSU Supercomputer PRIMEHPC FX1000 Rack Raysonho @ Open Grid Scheduler / Scalable Grid Engine - Eigenes Werk CC BY-SA 4.0

## Slide 6: RISC-V V ISA - A long journey
Early draft in 2015
Years of refinment. Frozen in end 2021.
Known programming model
RVV 0.5 proposal
RVV 1.0 frozen
RVV 0.6
RVV 0.7
RVV 0.8
RVV 0.9
2015
2021
Ara prototype
SiFive X280
RISC-V2
Vicuna
Vitruvius
AndesNX27V
Xuantie 910
Arrow
Comprehensive ISA (+300 instructions)
  VRF setup instructions (VL, element width, ...)
  Arithmetic instructions (int, fixpt, fp)
  Memory operations (unit-stride, strided, indexed)
  Predicated execution (masks)
  Permutation instructions (slide, reorder) Vector length agnostic – High reusability!

## Slide 7: EFCL Project Overview
Duration - 24 months
  Start: 03/21
  End: 03/23
Starting point
  AraV1 (RISC-V V draft v0.5)
  Peak performance/efficiency on matmul and conv2d for long vectors
Goals
  Expand benchmark pool with heterogeneous applications for high-dimensional workloads
  Update Ara from RISC-V V v0.5 to the most recent RISC-V Vector ISA (v0.9)
  Develop uArchitecture to improve IPC, Performance, Energy Efficiency
  Address coherence problem between Ara and Ariane
  HW/SW interface mixing intrinsics, hand-optimized macros, vector compilation

## Slide 8: EFCL Project Timeline, WPs, Milestones
Year 1
WP1: Workload analysis and benchmarking Select and implement key application kernels
WP2: uArch design and exploration of instruction extensions Develop the new micro-architecture compliant with RVV 0.9 (then RVV 1.0) Evaluate HW cost of ISA extensions to speed up key application kernels
Milestones: workload and benchmark analysis, version 0.1 of Ara2 with performance profiling
Year 2
WP3: uArch opt and implementation Optimize and implement microarchitecture Target frequency in the GHz range Emphasize scalability and high energy efficiency PPA of the resulting design
WP4: design space exploration, sw environment, open-source release Verify the design Provide Software support Open-source release of HW and SW
Milestones: version 1.0 of Arav2 with instruction extensions and PPA analysis, open source release of HW and SW

## Slide 9: EFCL Project Execution
Bi-weekly meetings
Rationale for SW selection
Discussed with companies, as representative of the target computation
Not too complex to ease vectorization, analysis, and insights
From RiVEC RVV benchmark suite too, to have comparable results
Stress different datapath units of Ara
Project WPs were mainly overlapped:
Specs update (to 0.9, then to 1.0) and new features require iterations on the physical implementation
Benchmarks required HW fixes and modifications, which require new iterations on the implementation
Verification done throughout the project, when adding new instructions, new benchmarks
The software ecosystem evolved throughout the project (compilers, simulator, V intrinsics, ...)
Updates needed to guarantee a high-quality open-source distribution

## Slide 10: RISC-V V ISA - A long journey
Early draft in 2015
Years of refinment. Frozen in end 2021.
Known programming model
RVV 0.5 proposal
RVV 1.0 frozen
RVV 0.6
RVV 0.7
RVV 0.8
RVV 0.9
2015
2021
Ara prototype
Ara RVV 0.9 Open-Source
Ara RVV 1.0
SiFive X280
RISC-V2
Vicuna
Vitruvius
AndesNX27V
Xuantie 910
Arrow
Comprehensive ISA (+300 instructions)
  VRF setup instructions (VL, element width, ...)
  Arithmetic instructions (int, fixpt, fp)
  Memory operations (unit-stride, strided, indexed)
  Predicated execution (masks)
  Permutation instructions (slide, reorder) Vector length agnostic – High reusability!

## Slide 11: Ara System – High-Level View
4B * #L
V-INSN
Ara 1GHz 2 * #L DP-GFLOPS
4 * #L GB/s
4B * #L
CVA6

## Slide 12: Ara System – One step below
Scalar core: CVA6

## Slide 13: Ara System – One step below
Scalar core: CVA6
Vector core: Ara

## Slide 14: Ara System – One step below
Scalar core: CVA6
Vector core: Ara
Same AXI interconnect

## Slide 15: Ara System – One step below
Scalar core: CVA6
Vector core: Ara
Same AXI interconnect
Parametric number of Lanes
  Each lane contains:
    FPU, ALU (computation)
    Chunk of the VRF (buffering)

## Slide 16: Ara System – One step below
Scalar core: CVA6
Vector core: Ara
Same AXI interconnect
Parametric number of Lanes
  Each lane contains:
    FPU, ALU (computation)
    Chunk of the VRF (buffering)

## Slide 17: Ara System – The Lane
Computational heart
  One 64-bit SIMD FPU/lane
  One 64-bit SIMD ALU/lane
Keep a chunk of the VRF
Maximize locality
  Element 0 remains in lane 0
  Minimize inter-lane communication
VRF in-lane reads/writes
16 Lanes: 32 DP-FLOP/Cycle – 128 HP-FLOP/Cycle!

## Slide 18: Ara System - The Lane
Modular VRF
4 KiB/lane
8 SRAM banks/lane
Operand queues
  Amortize VRF bank conflicts
VRF Chunk (4 KiB)

## Slide 19: Ara System – One step below
Scalar core: CVA6
Vector core: Ara
Same AXI interconnect
Parametric number of Lanes
  Each lane contains:
    FPU, ALU (computation)
    Chunk of the VRF (buffering)

## Slide 20: Ara System – One step below
Scalar core: CVA6
Vector core: Ara
Same AXI interconnect
Parametric number of Lanes
  Each lane contains:
    FPU, ALU (computation)
    Chunk of the VRF (buffering)
Memory coherence

## Slide 21: Ara System – One step below
Scalar core: CVA6
Vector core: Ara
Same AXI interconnect
Parametric number of Lanes
  Each lane contains:
    FPU, ALU (computation)
    Chunk of the VRF (buffering)
Memory coherence
Non-speculative interface

## Slide 22: Ara System – Working principles
CVA6 and Ara work in tandem!
CVA6 fetches scalar and vector instructions from memory
Scalar Instruction
Vector Instruction

## Slide 23: Ara System – Scalar instructions
Scalar Instruction

## Slide 24: Ara System – Scalar instructions
Scalar Instruction
Scalar execution – CVA6

## Slide 25: Ara System – Vector instructions
Vector Instruction

## Slide 26: Ara System – Vector instructions
Vector Instruction
Vector instruction dispatch

## Slide 27: Ara System – Vector instructions
Vector Instruction
Vector instruction dispatch
Top of the scoreboard
Non speculative!

## Slide 28: Ara System – Vector instructions
Vector Instruction
Vector instruction dispatch
Top of the scoreboard
Non speculative!
Ara answers back

## Slide 29: Ara System – Vector instructions
Vector Instruction
Vector instruction dispatch
Top of the scoreboard
Non speculative!
Ara answers back
No exceptions? CVA6 commits

## Slide 30: Ara System – Vector instructions
Vector Instruction
Vector instruction dispatch
Top of the scoreboard
Non speculative!
Ara answers back
No exceptions? CVA6 commits
Ara executes the instruction
Scalar Instruction

## Slide 31: Ara
Dispatcher (decode + CSRs)
Sequencer (issue + hazards)
Private VLSU (vload + vstore)
Slide Unit (permutations)
Mask Unit (predication)

## Slide 32: Ara
Dispatcher (decode + CSRs)
Sequencer (issue + hazards)
Private VLSU (vload + vstore)
Slide Unit (permutations)
Mask Unit (predication)
Lanes (computation + VRF)
Parametric number of lanes!
From 2 to 16

## Slide 33: Ara VRF
32 vregs
Ara 4 Lanes VRF
Size: 16 KiB
Split among the lanes!
128B
128B
128B
128B
.
.
.
.
.
.
.
.
.
.
.
.
L0
L1
L2
L3
v0
v31

## Slide 34: VRF – Monolithic vs. Split
mM
#B memory banks
#M masters
#S slaves #L lanes
xbar
xbar
xbar
xbar
xbar
xbar
xbar
xbar
b1
bB
m1
sS
s1
mM
m1
s1
sS
bB
b1
VRF
VRF chunk
VRF chunk
VRF chunk
Lane1
LaneL
Lane1
+

## Slide 35: Ara VRF
Vector with 8 elements
2 Byte/element

## Slide 36: Ara VRF
A0
A1
B0
B1
C0
C1
D0
D1
E0
E1
F0
F1
G0
G1
H0
H1
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
B15
Memory (outside Ara)
Vector with 8 elements
2 Byte/element

## Slide 37: Ara VRF
A0
A1
B0
B1
C0
C1
D0
D1
E0
E1
F0
F1
G0
G1
H0
H1
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
B15
Memory (outside Ara)
Vector with 8 elements
2 Byte/element
…
vld v0, (Memory)
…

## Slide 38: Ara VRF
L0
L1
L2
L3
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
B15
v0 (VRF, inside Ara)
A0
A1
B0
B1
C0
C1
D0
D1
E0
E1
F0
F1
G0
G1
H0
H1
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
B15
Vector with 8 elements
2 Byte/element
…
vld v0, (Memory)
…
Memory (outside Ara)
32 vregs
64B
64B
64B
64B
L0
L1
L2
L3
v0
v31

## Slide 39: Ara VRF
L0
L1
L2
L3
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
B15
v0 (VRF, inside Ara)
A0
A1
B0
B1
C0
C1
D0
D1
E0
E1
F0
F1
G0
G1
H0
H1
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
B15
A0
A1
Vector with 8 elements
2 Byte/element
…
vld v0, (Memory)
…
Memory (outside Ara)

## Slide 40: Ara VRF
L0
L1
L2
L3
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
B15
v0 (VRF, inside Ara)
A0
A1
B0
B1
C0
C1
D0
D1
E0
E1
F0
F1
G0
G1
H0
H1
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
B15
A0
A1
B0
B1
Vector with 8 elements
2 Byte/element
…
vld v0, (Memory)
…
Memory (outside Ara)

## Slide 41: Ara VRF
L0
L1
L2
L3
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
B15
v0 (VRF, inside Ara)
A0
A1
B0
B1
C0
C1
D0
D1
E0
E1
F0
F1
G0
G1
H0
H1
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
B15
A0
A1
B0
B1
C0
C1
Vector with 8 elements
2 Byte/element
…
vld v0, (Memory)
…
Memory (outside Ara)

## Slide 42: Ara VRF
L0
L1
L2
L3
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
B15
v0 (VRF, inside Ara)
A0
A1
B0
B1
C0
C1
D0
D1
E0
E1
F0
F1
G0
G1
H0
H1
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
B15
A0
A1
B0
B1
C0
C1
D0
D1
Vector with 8 elements
2 Byte/element
…
vld v0, (Memory)
…
Memory (outside Ara)

## Slide 43: Ara VRF
L0
L1
L2
L3
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
B15
v0 (VRF, inside Ara)
A0
A1
B0
B1
C0
C1
D0
D1
E0
E1
F0
F1
G0
G1
H0
H1
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
B15
A0
A1
E0
E1
B0
B1
C0
C1
D0
D1
Vector with 8 elements
2 Byte/element
…
vld v0, (Memory)
…
Memory (outside Ara)

## Slide 44: Ara VRF
L0
L1
L2
L3
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
B15
v0 (VRF, inside Ara)
A0
A1
B0
B1
C0
C1
D0
D1
E0
E1
F0
F1
G0
G1
H0
H1
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
B15
A0
A1
E0
E1
B0
B1
F0
F1
C0
C1
D0
D1
Vector with 8 elements
2 Byte/element
…
vld v0, (Memory)
…
Memory (outside Ara)

## Slide 45: Ara VRF
L0
L1
L2
L3
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
B15
v0 (VRF, inside Ara)
A0
A1
B0
B1
C0
C1
D0
D1
E0
E1
F0
F1
G0
G1
H0
H1
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
B15
A0
A1
E0
E1
B0
B1
F0
F1
G0
G1
C0
C1
D0
D1
Vector with 8 elements
2 Byte/element
…
vld v0, (Memory)
…
Memory (outside Ara)

## Slide 46: Ara VRF
L0
L1
L2
L3
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
B15
v0 (VRF, inside Ara)
A0
A1
B0
B1
C0
C1
D0
D1
E0
E1
F0
F1
G0
G1
H0
H1
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
B15
A0
A1
E0
E1
B0
B1
F0
F1
G0
G1
C0
C1
D0
D1
H0
H1
Vector with 8 elements
2 Byte/element
…
vld v0, (Memory)
…
Memory (outside Ara)

## Slide 47: Ara VRF
L0
L1
L2
L3
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
B15
v0 (VRF, inside Ara)
A0
A1
B0
B1
C0
C1
D0
D1
E0
E1
F0
F1
G0
G1
H0
H1
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
B15
A0
A1
E0
E1
B0
B1
F0
F1
G0
G1
C0
C1
D0
D1
H0
H1
Vector with 8 elements
2 Byte/element
…
vld v0, (Memory)
…
Memory (outside Ara)

## Slide 48: Ara VRF
L0
L1
L2
L3
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
B15
v0 (VRF, inside Ara)
A0
B0
C0
D0
E0
F0
G0
H0
B0
B1
B2
B3
B4
B5
B6
B7
A0
Vector with 8 elements
1 Byte/element
…
vld v0, (Memory)
…
B8
B9
B10
B12
B11
B14
B15
B13
B0
C0
D0
H0
G0
F0
E0
Memory (outside Ara)

## Slide 49: Differences between Ara1 and Ara2
Specs update (RVV0.5 -> RVV1.0)
  New VRF layout
  Mask Unit
  New insn encoding
Reshuffling support
Fixed-point support
Int + FP reductions
Barber's pole
CVA6 – more agnostic on V
Coherence/ordering protocol

## Slide 50: From Ara1 to Ara2 – ISA update
RVV 0.5
RVV 1.0
Polymorphic encoding
Compact ISA, harder decoding
Monomorphic encoding
Longer ISA, easier decoding

## Slide 51: From Ara1 to Ara2 – ISA update
RVV 0.5
Need for VRF state to decode instruction
CVA6 was not vector agnostic
V-decoder in CVA6
RVV 1.0
Easier to decode instructions
CVA6 needs only minimal information to process V instructions
Push V-related hardware in Ara!

## Slide 52: From Ara1 to Ara2 – ISA update​
RVV 0.5
RVV 1.0
Reg enable/length modified at runtime
Data-type per register
Constrained VRF setting
Data-type agnostic

## Slide 53: From Ara1 to Ara2 – ISA update​
Simpler VRF configuration
VRF configuration is now static
32 vector registers, but they can be merged in groups of 2, 4, 8 registers (LMUL parameter == 2, 4, 8)
Interpret vector registers depending on SEW (single-element width) only

## Slide 54: From Ara1 to Ara2 – ISA update
RVV 0.5
RVV 1.0
Mask bits aligned with elements
Mask bits compressed
Need for a dedicated unit that packs-unpacks mask bits - MASKU

## Slide 55: From Ara1 to Ara2 – ISA update
Some units access the whole VRF
Each unit is connected to all the lanes (in and out)
All-to-all connected units:
  VLSU
  SLDU
  MASKU (new!)
All-to-all connected units complicate rounting

## Slide 56: Coherence/ordering protocol
Before
No hardware solution
Need for software fences
Memory Ordering
If vector store is ongoing block scalar loads/stores
If scalar store ongoing block vector loads/stores
If scalar/vector load is ongoing block vector/scalar stores
Cache coherence
Invalidate scalar cache lines upon vector store

## Slide 57: Vector Reductions
Before
No vector reductions
After the update
Integer reduction
Floating-Point (FP) reduction
Ordered FP reduction

## Slide 58: Vector Reductions
e0 | e1 | e2 | e3 | e4 | e5 | e6 | e7 | e8 | e9 | e10 | e11
vs1
vs2
s0 | - | - | - | - | - | - | - | - | - | - | -
vd
r0 | - | - | - | - | - | - | - | - | - | - | -
Notes: Which instructions

## Slide 59: Vector Reductions
r0 = s0 + e0 + e1 + e2 + … + e11
Example: vredsum vd, vs1, vs2
e0 | e1 | e2 | e3 | e4 | e5 | e6 | e7 | e8 | e9 | e10 | e11
vs1
vs2
s0 | - | - | - | - | - | - | - | - | - | - | -
vd
r0 | - | - | - | - | - | - | - | - | - | - | -
Notes: Which instructions

## Slide 60: Vector Reductions
r0 = s0 + e0 + e1 + e2 + … + e11
Example: vredsum vd, vs1, vs2
e0 | e1 | e2 | e3 | e4 | e5 | e6 | e7 | e8 | e9 | e10 | e11
vs1
vs2
s0 | - | - | - | - | - | - | - | - | - | - | -
vd
r0 | - | - | - | - | - | - | - | - | - | - | -
Notes: Which instructions

## Slide 61: Vector Reductions – Intra-lane phase start
e0 | e4 | e8
e1 | e5 | e9
e2 | e6 | e10
e3 | e7 | e11
s0
LANE 0
LANE 1
LANE 2
LANE 3
e0 | e1 | e2 | e3 | e4 | e5 | e6 | e7 | e8 | e9 | e10 | e11
s0
vs1
vs2
vs1
vs2
Notes: Which instructions

## Slide 62: Vector Reductions
LANE 0
LANE 1
LANE 2
LANE 3
vs1
vs2
ALU
ALU
ALU
ALU
temp0 = s0 + e0 + e4 + e8
temp1 = e1 + e5 + e9
temp2 = e2 + e6 + e10
temp3 = e3 + e7 + e11
e0 | e4 | e8
e1 | e5 | e9
e2 | e6 | e10
e3 | e7 | e11
s0
Notes: Which instructions

## Slide 63: Vector Reductions
ALU
s0
e8
e4
e0
LANE 0
Notes: Which instructions

## Slide 64: Vector Reductions
ALU
e8
e4
e0
+
e0 + s0
s0
LANE 0
Notes: Which instructions

## Slide 65: Vector Reductions
ALU
e8
e0 + s0
e4
+
e0 + s0 + e4
LANE 0
Notes: Which instructions

## Slide 66: Vector Reductions
ALU
e8
+
e0 + s0 + e4 + e8
e0 + s0 + e4
LANE 0
Notes: Which instructions

## Slide 67: Vector Reductions – Intra-Lane phase end
LANE 0
LANE 1
LANE 2
LANE 3
temp0
ALU
ALU
ALU
ALU
temp0 = s0 + e0 + e4 + e8
temp1 = e1 + e5 + e9
temp2 = e2 + e6 + e10
temp3 = e3 + e7 + e11
temp2
temp1
temp3
Notes: Which instructions

## Slide 68: Vector Reductions – Inter-Lane phase start
LANE 0
LANE 1
LANE 2
LANE 3
temp0
temp2
temp1
temp3
L0
L1
Notes: Which instructions

## Slide 69: Vector Reductions
LANE 0
LANE 1
LANE 2
LANE 3
temp0
temp2
temp1
temp3
Notes: Which instructions

## Slide 70: Vector Reductions
LANE 0
LANE 1
LANE 2
LANE 3
temp1
temp0
temp3
temp2
Notes: Which instructions

## Slide 71: Vector Reductions
LANE 0
LANE 1
LANE 2
LANE 3
temp01
temp23
temp01 = temp0 + temp1
temp23 = temp2 + temp3
Notes: Which instructions

## Slide 72: Vector Reductions
LANE 0
LANE 1
LANE 2
LANE 3
temp01
temp23
Notes: Which instructions

## Slide 73: Vector Reductions
LANE 0
LANE 1
LANE 2
LANE 3
temp0123
temp0123 = temp01 + temp23
Notes: Which instructions

## Slide 74: Vector Reductions
LANE 0
LANE 1
LANE 2
LANE 3
temp0
ALU
ALU
ALU
ALU
temp2
temp1
temp3
SLIDE
UNIT
Notes: Which instructions

## Slide 75: Vector Reductions
SLIDE
UNIT
LANE 0
LANE 1
LANE 2
LANE 3
temp0
ALU
ALU
ALU
ALU
temp2
temp1
temp3
Notes: Which instructions

## Slide 76: Vector Reductions
SLIDE
UNIT
LANE 0
LANE 1
LANE 2
LANE 3
temp0
ALU
ALU
ALU
ALU
temp2
temp1
temp3

## Slide 77: Vector Reductions – Inter-Lane phase end
SLIDE
UNIT
LANE 0
LANE 1
LANE 2
LANE 3
temp0
ALU
ALU
ALU
ALU
temp2
temp1
temp3
Notes: Which instructions

## Slide 78: Vector Reductions – SIMD phase start
ALU
LANE 0
temp0123
64-bit
Notes: Which instructions

## Slide 79: Vector Reductions
ALU
LANE 0
h0 | h1 | h2 | h3
64-bit
Reduce the 64-bit packet of N elements
Example: four 16-bit elements
log2(N) operations for N sub-elements
Example: log2(4) = 2 operations
Notes: Which instructions

## Slide 80: Vector Reductions
ALU
LANE 0
h0 | h1
h2 | h3
+
h01 | h23
First operation
Reduce the 64-bit packet of N elements
Example: four 16-bit elements
log2(N) operations for N sub-elements
Example: log2(4) = 2 operations
Notes: Which instructions

## Slide 81: Vector Reductions – SIMD phase end
ALU
LANE 0
h01
h23
+
h0123
16-bit
Second operation
Reduce the 64-bit packet of N elements
Example: four 16-bit elements
log2(N) operations for N sub-elements
Example: log2(4) = 2 operations
Notes: Which instructions

## Slide 82: Floating-point reductions?
FPUs are pipelined! Pipeline levels (R) depend on SEW
Wait R cycles before a new operation?
Trick: use pipeline registers to store partial accumulators
In the end: final round of accumulation
Intra-Lane reduction latency
For R power of 2 (superlinear)
FPU
Op0
Op1
Op2
FPU
Op0 + Op1
Op2
...
Op3
Op4
Op5
FPU
Op0 + Op1 + Op4
Op2
Op3
Op5
FPU
Op0 + Op1
Op2
Op3
Op4
Op5
Op6
...
...

## Slide 83: Verification and Software Eco-System
Verification
Update and extend riscv-tests repository
Every instruction has its own set of dedicated tests
Multiple self-verifying benchmarks implemented
Additional tests from external company
CI integrated on GitHub
Software eco-system
LLVM compiler + SPIKE updated more than once to follow specs update
Vector intrinsics support - Still in evolution from RISC-V community!
Verilator (open-source) to simulate the system
Initial support for auto-vectorization

## Slide 84
RTL
Sim
Benchmarks
Linear Algebra, math: fmatmul, fconv2d, jacobi2d, dotp, exp, log, cos
Routing Algorithm: pathfinder
DSP: fft, dwt
ML: softmax, roi_align, dropout
AWB, spmv, ReLu, ... : not in the analysis
Throughput
vs. number of lanes (2, 4, 8, 16)
vs. vector length (4, 8, 16, 32, 64, 128 elements)
How scalar core and memory system influence performance?
Evaluation

## Slide 85
RTL
gf22
Sim
Synth
P&R
PPA metrics
Benchmarks
LA: fmatmul, fconv2d, jacobi2d, dotp, exp
RA: pathfinder
DSP: fft, dwt
ML: softmax, roi_align, dropout
Throughput
vs. number of lanes
vs. vector length
How scalar core and memory system influence performance?
Physical implementation
PPA metrics
Efficiency study
Scaling analysis
Evaluation

## Slide 86: System performance – A focus on matmul
Up to 32 DP-FLOP/cycle
  With 16 Lanes
FP-matmul
  A[N][N] * B[N][N]

## Slide 87: System performance – A focus on matmul
Up to 32 DP-FLOP/cycle
  With 16 Lanes
FP-matmul
  A[N][N] * B[N][N]
  X-axis: Matrix Size N
Increasing arithmetic intensity!

## Slide 88: System performance – A focus on matmul
Up to 32 DP-FLOP/cycle
  With 16 Lanes
FP-matmul
  A[N][N] * B[N][N]
  X-axis: Matrix Size N
  Always computation-bound
Increasing arithmetic intensity!

## Slide 89: System performance – A focus on matmul
Up to 32 DP-FLOP/cycle
  With 16 Lanes
FP-matmul
  A[N][N] * B[N][N]
  X-axis: Matrix Size N
  Always computation-bound
Longer vector, better performance
  Amortize setup time for V instruction
  Amortize CVA6 non-idealities
>98.5% FPU Utilization

## Slide 90: Issue-rate limitation
There is another intrinsic limitation to performance
Issue-rate limitation:
4-element vector
4-lane Ara (4 FPUs)
Max Throughput = 1 vfmacc/cycle
To reach full performance, Ara would need 1 vfmacc per cycle!
BUT, in the best case: 1 vfmacc every 3 cycles
// Loop kernel is a sequence of:
// bump pointer
add addr, 8
// load scalar from mtx A
ld x, @addr
// issue vfmacc
vfmacc v0, v1, x

## Slide 91: System performance – A focus on matmul
Issue-rate limitation hits short/medium-vectors
Longer vectors hide CVA6's non-ideal issue-rate latency
i.e., with longer vectors, Ara does not starve

## Slide 92: System performance – A focus on matmul
RVV 0.5:
2 instructions for vector-scalar operation
Issue-rate: 1/5 cycles
RVV 1.0:
1 instruction for vector-scalar operation
Issue-rate: 1/4 cycles

## Slide 93: Software
Kernel | Domain | Format | Compute bound | Mask | Slide | Stride Mem | Idx Mem | Reduction | Max Perf [DP-FLOP/cycle]
matmul | Linear Algebra, ML | FP64, int64 | Y | N | N | N | N | N | 1 × 2.0 × L
conv2d | Signal Processing, ML | FP64, int64 | Y | N | Y | N | N | N | 1 × 2.0 × L
dotproduct | Linear Algebra | FP64, int64 | Y | N | N | N | N | Y | 1 × 0.5 × L*
jacobi2d | Stencil | FP64 | Y | N | Y | N | N | N | 1 × 1 × 1.0 × L
dropout | ML | FP32 | N | Y | N | N | N | N | 2 × 0.25 × L
fft | Signal Processing, | FP32 | Y | Y | Y | N | Y | N | 2 × 5/4 × L
dwt | Signal Processing, | FP32 | N | N | N | Y | N | N | 2 × 0.5 × L
pathfinder | Routing Algorithm | int32 | N | Y | N | N | N | N | 2 × 1.0 × L
exp | Scientific, ML | FP64 | Y | N | N | N | N | N | 1 × 28/21 × L
softmax | ML | FP32 | Y | N | N | N | N | Y | 2 × 32/25 × L
roi-align | ML | FP32 | N | N | N | N | N | N | 2 × 3/5 × L

## Slide 94: Software
Kernel | Domain | Format | Compute bound | Mask | Slide | Stride Mem | Idx Mem | Reduction | Max Perf [DP-FLOP/cycle]
matmul | Linear Algebra, ML | FP64, int64 | Y | N | N | N | N | N | 1 × 2.0 × L
conv2d | Signal Processing, ML | FP64, int64 | Y | N | Y | N | N | N | 1 × 2.0 × L
dotproduct | Linear Algebra | FP64, int64 | Y | N | N | N | N | Y | 1 × 0.5 × L*
jacobi2d | Stencil | FP64 | Y | N | Y | N | N | N | 1 × 1 × 1.0 × L
dropout | ML | FP32 | N | Y | N | N | N | N | 2 × 0.25 × L
fft | Signal Processing | FP32 | Y | Y | Y | N | Y | N | 2 × 5/4 × L
dwt | Signal Processing | FP32 | N | N | N | Y | N | N | 2 × 0.5 × L
pathfinder | Routing Algorithm | int32 | N | Y | N | N | N | N | 2 × 1.0 × L
exp | Scientific, ML | FP64 | Y | N | N | N | N | N | 1 × 28/21 × L
softmax | ML | FP32 | Y | N | N | N | N | Y | 2 × 32/25 × L
roi-align | ML | FP32 | N | N | N | N | N | N | 2 × 3/5 × L

## Slide 95: Throughput ideality
Benchmark performance analysis
Throughput ideality = Throughput/Max_Throughput
It measures degree of ideality of the Ara system for that kernel from 0% to 100%
Throughput ideality strongly depends on number of lanes and vector length
>50% of performance on average from 16 Elements/Lane on
>75% of performance from 8 Elements/Lane for highly intensive kernels (fmatmul, fconv2d, ~jacobi2d)
Notes: Update kernel plots and update

## Slide 96: Throughput ideality - Byte/Lane ratio
Throughput ideality
i.e., actual/ideal performance
Measure of how ideally Ara behaves
The longer the vector, the better the throughput ideality (until peak)
How long is a "sufficiently long" vector?
Performance ideality correlated with Byte/Lane ratio (~Element/Lane)
Same computational efficiency with 2*L? Our vector should be as twice as long
i.e., to double performance, we need a longer vector too

## Slide 97: Performance analysis
Ara2 suffers from short/medium vector performance loss
Who to blame? CVA6? Memory System? Vector accelerator?
Analyze three systems
  CVA6 + Scalar I/D$ + Ara
    Show limitations due to the whole system
  CVA6 + Ideal I/D$ + Ara
    Show limitations due to CVA6 and Ara
  Ideal CVA6 + Ideal I/D$ + Ara
    Show limitations due to Ara
Mem
Ara
CVA6
I$
Ideal
Mem
Ara
CVA6
D$
Ideal
Mem
Ara
Ideal

## Slide 98: Performance analysis
Ara2 suffers from short/medium vector performance loss
Who to blame? CVA6? Memory System? Vector accelerator?
Analyze three systems
  CVA6 + Scalar I/D$ + Ara
    Show limitations due to the whole system
  CVA6 + Ideal I/D$ + Ara
    Show limitations due to CVA6 and Ara
  Ideal CVA6 + Ideal I/D$ + Ara
    Show limitations due to Ara
Mem
Ara
CVA6
I$
Inf size
uncoherent
Mem
Ara
CVA6
D$
Mem
Ara
V insn FIFO
Ideal dispatcher system
Ideal cache
system
Default/vanilla
system

## Slide 99: CVA6 influence on performance
Ideal dispatcher does not improve performance much!
(2-lane Ara, 8-element vector)
Almost no performance gain for long vectors
(2-lane Ara, 128-element vector)

## Slide 100: CVA6 influence on performance
16 lanes, 128 elements case
Correlation with D$ misses even more evident

## Slide 101: CVA6 influence on performance
The performance gain should be attributed to the ideal caches, and not to the ideal CVA6!
All three kernels rely on scalar forwarding from scalar to vector core!
D$ misses heavily affect performance!
fmatmul, fconv2d
Source and destination separated in memory
Problem: cache line/bus size
jacobi2d:
Iterative algorithm
Elements written by vector store get read back from the scalar core (from the D$!)
Problem: scalar cache

## Slide 102: Scalar D$ influence on performance
AXI data-width
D$ line-width
Ara2
CVA6
AXI xBAR
From 42% to 72%!
16 Lanes, fmatmul, n = 16
Throughput ideality vs.
  AXI data-width
  D$ line-width
Miss penalty
Hit rate
Miss penalty
AXI data-width

## Slide 103: Main performance drivers
Absolute fmatmul performance of a 4-lane Ara
Different performance drivers for different sizes
Orange and violet are merged gains
Huge CVA6 impact with short vectors only
Caches play a role for medium vectors
Long vectors are already at their peak
Issue-Rate limitation does not hold for ideal CVA6, but holds for the real system!

## Slide 104: Ara wants more Computational Power
2 FPUs
4 FPUs
8 FPUs
16 FPUs
FPUs per Ara

## Slide 105: Ara wants more Computational Power
2 FPUs
4 FPUs
8 FPUs
16 FPUs
1 Ara
2 Ara
exploration
Both systems have 16 FPUs
FPUs per Ara
Number of Aras
4 Ara

## Slide 106: Single core vs. Multi core
Increase Byte/Lane ratio with Multi-Core?
Exploit second dimension!

## Slide 107: Single core vs. Multi core system
16 FPU system in different flavors
1C16L: one 16-lane Ara
8C2L: eight 2-lane Ara
e.g., 32x32x32 matmul performance
32 elements processed by a single 16-lane Ara
under-utilize the system's resources (2 Elm/Lane)
Eight 2-lane Aras exploit the second dimension of the matrix to speed up the computation (16 Elm/Lane)
The issue-rate limitation does not exist for 8C2L
32

## Slide 108: Physical Implementation
GF22 FDX FD-SOI
SS frequency: 950 MHz
TT frequency: 1.35 GHz
Efficiency: 37.8 DP-GFLOPS/W
  1.35GHz, fp-matmul
0.95 mm2
1 mm2

## Slide 109: Physical Implementation

## Slide 110: Physical Implementation

## Slide 111: Physical Implementation – Scaling up
Scale up with the number of lanes
Flat flow for #L > 8

## Slide 112: PPA Metrics
AraV2 (Arav1) | 2 lanes | 4 lanes | 8 lanes | 16 lanes*
SS Frequency [MHz] | 950 (920) | 960 (930) | 940 (870) | 860 (780)
TT Frequency [GHz] | 1.35 (1.25) | 1.35 (1.25) | 1.35 (1.17) | 1.26 (1.04)
Die Area (mm2) | 0.588 | 0.953 | 1.876 | 4.47
Cell+Macro Area (mm2) | 0.455 (0.443) | 0.734 (0.683) | 1.346 (1.174) | 2.559 (2.136)
Macro Area (mm2) | 0.111 | 0.153 | 0.235 | 0.4
Peak Efficiency | 34.1 (35.6) | 37.7 (37.8) | 35.7 (39.9) | 30.3 (40.8)
*Simplified Mask Unit
Improved SS, TT frequency
Smaller die, slightly higher Cell+Macro area (with added functionality)
Same efficiency up to 4 lanes, then the trend is different
RVV 0.5 gains in efficiency until 16 lanes
Efficiency peak at 4 lanes for RVV 1.0 design

## Slide 113: Area breakdown
Area [kGE] | 2L | 4L | 8L | 16L | 16L*
CVA6 | 894 | 896 (1.0×) | 906 (1.0×) | 904 (1.0×) | 904 (1.0×)
Lane | 612 | 617 (1.0×) | 626 (1.0×) | 628 (1.0×) | 573 (0.9×)
Dispatcher | 16 | 17 (1.1×) | 19 (1.1×) | 23 (1.2×) | 20 (1.1×)
Sequencer | 14 | 15 (1.1×) | 17 (1.2×) | 29 (1.6×) | 29 (1.6×)
MASKU | 38 | 97 (2.5×) | 300 (3.1×) | 1105 (3.7×) | 442 (1.5×)
ADDRGEN | 35 | 36 (1.0×) | 44 (1.2×) | 59 (1.3×) | 60 (1.4×)
VLDU | 15 | 45 (3.0×) | 212 (4.7×) | 1286 (6.1×) | 1135 (5.4×)
VSTU | 8 | 21 (2.8×) | 64 (3.1×) | 332 (5.2×) | 342 (5.3×)
New SLDU | 24 | 48 (2.0×) | 94 (2.0×) | 196 (2.1×) | 190 (2.1×)
Old SLDU | 39 | 131 (3.4×) | 577 (4.4×) | 2900 (5.0×) | 2860 (5.0×)

## Slide 114: uArch optimization: Slide Unit
SLDU made scaling up to 16 lanes impossible
Exponential growth after P&R
All-to-all byte connections scale ~L^2
Do we need to support whichever slide amount?
Area [kGE] | 2L | 4L | 8L | 16L
New SLDU | 24 | 48 (2.0×) | 94 (2.0×) | 196 (2.1×)
Old SLDU | 39 | 131 (3.4×) | 577 (4.4×) | 2900 (5.0×)

## Slide 115: uArch optimization: Slide Unit
SLDU made scaling up to 16 lanes impossible
Exponential growth
All-to-all byte connections scale ~L^2
Do we need to support whichever slide amount?
Solution
Support only power-of-2 slide amounts
Either reshuffle OR slide
Area [kGE] | 2L | 4L | 8L | 16L
New SLDU | 24 | 48 (2.0×) | 94 (2.0×) | 196 (2.1×)
Old SLDU | 39 | 131 (3.4×) | 577 (4.4×) | 2900 (5.0×)

## Slide 116: Power breakdown
4 Lanes
FP-matmul computational loop

## Slide 117: Power breakdown
4 Lanes
FP-matmul computational loop
11% power to CVA6

## Slide 118: Power breakdown
4 Lanes
FP-matmul computational loop
>80% power to the Lanes

## Slide 119: Power breakdown
4 Lanes
FP-matmul computational loop

## Slide 120: Power breakdown
4 Lanes
FP-matmul computational loop
~30% Buffering

## Slide 121: Power breakdown
4 Lanes
FP-matmul computational loop
55% Actual Computation

## Slide 122: Energy Efficiency
Boost energy efficiency
Clock-gate unused CVA6 memory banks, VRF banks
Operand-gate the SIMD multipliers
Clock-gate the SIMD multipliers when not used
Ara 4 Lanes, fmatmul A[128][128] x [128][1KiB] = C[128][1KiB]
Fmt Eff
fp64 37.74 DP-FLOPS/W
fp32 90.04 SP-FLOPS/W
fp16 195.86 HP-FLOPS/W
int64 38.32 DP-GOPS/W
int32 85.26 SP-GOPS/W
int16 180.56 HP-GOPS/W
int8 376.04 BP-GOPS/W

## Slide 123: ISA extension – Transformers and small Matmul
Improve small-size matmul?
Default algorithm
  Example: 32x32x32 fp32-matmul (4*32) output tile 4-Lane Ara
  4 scalar loads (D$ misses)
  4 vmacc instructions (4 setup time, issue-rate limitation)
  4 Elements/Lane -> 16 B/Lane
FPU
FPU
FPU
FPU
L0
L3
L1
L2

## Slide 124: ISA extension – Transformers and small Matmul
Improve small-size matmul?
Matrix algorithm
  Example: 32x32x32 fp32-matmul (4*32) output tile 8-Lane Ara
  0 scalar loads (no D$ misses)
  1 mmacc instruction (1 setup time)
  32 Elements/Lane -> 64 B/Lane
FPU
FPU
FPU
FPU
L0
L3
L1
L2
Broadcast

## Slide 125: ISA extension – Transformers and small Matmul
Improve small-size matmul?
Default algorithm vs. Optimized Matrix algorithm
Default
Optimized
Matmul Utilization (4 Lanes)
Peak of 2x performance for small problems!!

## Slide 126: ISA extension – Transformers and small Matmul
Trial on 2, 4, 8 lanes – No frequency loss, negligible area impact
What about Energy Efficiency? 4-lane Ara example
Peak of +75% EE improvement on small problems!

## Slide 127: SoA Comparison
Vitruvius+
  8-lane processor
  ~ Max frequency for 8 Lanes
  ~ IPC on jacobi2d, matmul, pathfinder
  Unfair power comparison (no scalar core? No caches? How data are generated?)
  Vicuna
    int-only RVV1.0
    ~ utilization on matmul
    FPGA only PPA metrics
  Hwacha
    ~ utilization on matmul
    Chip-level Power, hard to compare

## Slide 128: Yun: Ara’s in tsmc65
Yun - tsmc65
Ara – 4 Lanes
SoC Architecture
  Ara System
  64 KiB SRAM Memory
  JTAG + Debug Module
  Double-precision FPU
  Die area: 6 mm2
  Frequency: ~250 MHz
Already tested: it works!

## Slide 129: What's further?
OS support
  Virtual memory
    Re-use CVA6's MMU
    Separate TLB for V accesses?
  Context switch
    Restrict V core to one process only
    Faster context switch
  Exceptions
    Extensive debug
CVA6
Ara
Memory
MMU
VLSU
vld (virtual @)
vld req (physical @)
@ translation

## Slide 130: What's further?
Matrix Extension
  Load matrices instead of vectors
  Decouple Scalar-Vector processors
    Bypass D$!
  Increase #operations/#instruction ratio
    Pay less start-up time cycles
  Reduce VRF accesses

## Slide 131: What's further?
Ara OpenPITON – PolAra
Ara in real multi-core environment
Optimizing matmul on L2-sparse memory hierarchy
https://github.com/openhwgroup/core-v-polara-apu/tree/openpiton_polara

## Slide 132: Project goals
Expand benchmark pool with heterogeneous applications for high-dimensional workloads
  Extended benchmark pool with heterogeneous set of kernels and program to stress different units of Ara2
  Performance analysis for each kernel and degree of ideality w.r.t. the maximum achievable
Update Ara from RISC-V V v0.5 to the most recent RISC-V Vector ISA (v0.9)
  Ara updated to RISC-V V v1.0 frozen
  Added RVV features missing from AraV1 (e.g., int- and fp-reductions)
Develop uArchitecture to improve IPC, Performance, Energy Efficiency
  uArchitectural optimization (e.g., SLDU optimization) to scale up to 8 and 16 lanes
  Exploration of new ISA extension to speed up transformer models
  Transprecision FPU down to 16 bit, ready to host 16alt and 8-bit formats
  Higher performance (frequency), same Energy Efficiency for smaller Ara instances
Address coherence problem between Ara and Ariane
  Added coherence and memory ordering engine
HW/SW interface mixing intrinsics, hand-optimized macros, vector compilation
  Compiler support with RVV intrinsics
  Benchmark pool and optimized programs with intrinsics, hand-optimized macros, and possibly auto-vectorization

## Slide 133: Publications
Published:
ASAP 2022 Conference
Title: A “New Ara” for Vector Computing: An Open Source Highly Efficient RISC-V V 1.0 Vector Processor Design
Authors: Matteo Perotti, Matheus Cavalcante, Nils Wistoff, Renzo Andri, Luca Benini
Link: https://ieeexplore.ieee.org/abstract/document/9912071
Work in progress:
IEEE Journal TCOMP

## Slide 135: EFCL Project Timeline, WPs, Milestones
Year 1
WP1: Workload analysis and benchmarking Select target sensors and key algorithms - develop a benchmark suite with performance targets for key application kernels used in multi-dimensional sensor processing and fusion for consumer devices.
WP2: uArch design and exploration of instruction extensions Moving from ARAv1 develop the new micro-architecture supporting the standard ISA and evaluate the impact in HW cost and performance benefits of instruction extensions targeted to the workloads in WP1.
Milestones: workload and benchmark analysis, version 0.1 of Ara2 with performance profiling
Year 2
WP3: uArch opt and implementation Moving from version 0.1 the goal is to develop an optimized microarchitecture, design with a target frequency in the GHz range and support for the ISA extension explored in WP2. The design will emphasize scalability to large lane count and high energy efficiency. PPA of the resulting design will be assessed
WP4: design space exploration, sw environment, open-source release The main goal of this WP is to verify the design of VP4, provide software support (intrinsics, optimized libraries, preliminary support for vectorization). An open-source release of HW and SW will be prepared with documentation.
Milestones: version 1.0 of Arav2 with instruction extensions and PPA analysis, open source release of HW and SW

## Slide 136: Often need for more buffering space
Program (matmul)
3x3
Matrix Tile
Matrix A
Matrix B
Matrix C
Memory
Scalar
Register File
Pointers
Chart: Matmul Kernel
| 6x6 | 5x5 | 4x4 | 3x3 | 2x2 | 1x1
Relative Runtime | 0.28071 | 0.26173 | 0.22691 | 0.19626 | 0.23504 | 1
Housekeeping
6x6
Matrix Tile
The tile does not fit

## Slide 137: Vector Register File (VRF) – L0 buffer
Program (matmul)
Matrix A
Matrix B
Matrix C
Memory
3x3
Matrix Tile
Scalar
Register File
Pointers
Housekeeping
Scalar
Data
Large Matrix Tile
Vector Register File
VLEN

## Slide 138: VRF – L0 buffer
Program (matmul)
Matrix A
Matrix B
Matrix C
Memory
3x3
Matrix Tile
Pointers
Housekeeping
Scalar
Data
VEC
SCALAR CORE
RF
Large Matrix Tile
Vector Register File

## Slide 139: SIMD computation – tackle the VNB
Program (matmul)
Matrix A
Matrix B
Matrix C
Memory
3x3
Matrix Tile
Pointers
Housekeeping
Scalar
Data
VEC
SCALAR CORE
RF
Large Matrix Tile
Vector Register File
1 Instruction
MUCH computation

## Slide 140: SIMD computation – tackle the VNB
Program (matmul)
Matrix A
Matrix B
Matrix C
Memory
3x3
Matrix Tile
Pointers
Housekeeping
Scalar
Data
VEC
SCALAR CORE
RF
Large Matrix Tile
Vector Register File
64
64
64

## Slide 141: Example of vector code
// Scalar code
for (int i = N; i > 0; --i) {
ld a
ld b
add(c, a, b)
st c
// bump pointers
}
Vector Addition
C[i]=A[i]+B[i]
Why Vector?
  Reduce Von-Neumann Bottleneck
  Higher buffering capabilities
  Vector length agnostic, reduced ISA
Notes: 45 s

## Slide 142: Example of vector code
// Scalar code
for (int i = N; i > 0; --i) {
ld a
ld b
add(c, a, b)
st c
// bump pointers
}
// Vector code
for (int vl = get_vl(N); N > 0; N -= vl) {
vld va
vld vb
vadd(vc, va, vb)
vst vc
// bump pointers and get vl
}
Vector Addition
C[i]=A[i]+B[i]
Why Vector?
  Reduce Von-Neumann Bottleneck
  Higher buffering capabilities
  Vector length agnostic, reduced ISA

## Slide 143: Example of vector code
// Scalar code
for (int i = N; i > 0; --i) {
ld a
ld b
add(c, a, b)
st c
// bump pointers
}
// Vector code
for (int vl = get_vl(N); N > 0; N -= vl) {
vld va
vld vb
vadd(vc, va, vb)
vst vc
// bump pointers and get vl
}
Why Vector?
  Reduce Von-Neumann Bottleneck
  Higher buffering capabilities
  Vector length agnostic, reduced ISA
2N/vl loads
N/vl add
N/vl stores
2N loads
N add
N stores
4N FETCHED, DECODED
4N/vl FETCHED, DECODED
Vector Addition
C[i]=A[i]+B[i]
Scalar – 1 instruction == 1 operation
Vector – 1 instruction == [vl] operations

## Slide 144: Example of vector code
// Scalar code
for (int i = N; i > 0; --i) {
ld a
ld b
add(c, a, b)
st c
// bump pointers
}
// Vector code
for (int vl = get_vl(N); N > 0; N -= vl) {
vld va
vld vb
vadd(vc, va, vb)
vst vc
// bump pointers and get vl
}
2N/vl loads
N/vl add
N/vl stores
2N loads
N add
N stores
4N FETCHED, DECODED
4N/vl FETCHED, DECODED
Vector Addition
C[i]=A[i]+B[i]
Scalar – 1 instruction == 1 operation
Vector – 1 instruction == [vl] operations
Lower pressure on memory!
Less power required!
Why Vector?
  Reduce Von-Neumann Bottleneck
  Higher buffering capabilities
  Vector length agnostic, reduced ISA

## Slide 145: RVV < 1.0 - SLEN parameter
RVV < 1.0
VLEN: size of a single vector register (bits)
SLEN: size of a chunk of a vector register in a lane (bits)
SEW: single element width (bits)
SLEN = VLEN/#Lanes
Lane-friendly
Successive elements in successive lanes
Example: VLEN = 128 bit SLEN = 64 bit
32 vregs
8B
8B
L0
L1
v0
v31
SEW

## Slide 146: RVV 1.0 - No SLEN parameter
RVV 1.0
VLEN: size of a single vector register (bits)
SEW: single element width (bits)
VRF Byte layout == Memory Byte layout
Non Lane-friendly
Widening instructions become a problem
During a widening, elements would need to be moved across lanes
To ease widening instructions, we mimick an SLEN parameter.
But we need to be able to reconstruct the vector as if it was buffered without SLEN!

## Slide 147: Byte mapping (memory – VRF)
L0
L1
L2
L3
L0
L1
L2
L3
MAPPING
Memory(B1) - v0(B1, L0)
MAPPING
Memory(B1) - v0(B0, L1)
B0
B1
B0
B1
EW8
EW16
…
vld v0, (Memory)
…
…
vld v0, (Memory)
…
B0
B1
B0
B1
v0
v0
Memory
Memory

## Slide 148: Byte mapping (memory – VRF)
L0
L1
L2
L3
L0
L1
L2
L3
MAPPING
v0(B0, L1) - Memory(B2)
MAPPING
v0(B0, L1) - Memory(B1)
B0
B1
B0
B1
EW8
EW16
…
vst v0, (Memory)
…
…
vst v0, (Memory)
…
B0
B1
v0
Memory
B2
B3
B0
B1
Memory
B2
B3

## Slide 149: Ara VRF
L0
L1
L2
L3
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
B15
v0 (VRF, inside VU1.0)
A0
A1
B0
B1
C0
C1
D0
D1
E0
E1
F0
F1
G0
G1
H0
H1
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
B15
Memory (outside Ara)
A0
A1
E0
E1
B0
B1
F0
F1
G0
G1
C0
C1
D0
D1
H0
H1
Vector with 8 elements
2 Byte/element
…
vld v0, (Memory)
…
MAPPING
v0 (EW16)

## Slide 150: Ara VRF
L0
L1
L2
L3
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
B15
v0 (VRF, inside VU1.0)
Vector with 1 elements
1 Byte/element
…
vld v0, (Memory)
…
A0
B0
B1
B2
B3
B4
B5
B6
B7
Memory (outside Ara)
B8
B9
B10
B12
B11
B14
B15
B13
E0
E1
F0
F1
G0
G1
H0
H1
A0
MAPPING
v0 (EW8)
A1
B0
B1
C0
C1
D0
D1

## Slide 151: Ara VRF
L0
L1
L2
L3
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
B15
v0 (VRF, inside VU1.0)
Vector with 1 elements
1 Byte/element
…
vld v0, (Memory)
…
A0
B0
B1
B2
B3
B4
B5
B6
B7
Memory (outside Ara)
B8
B9
B10
B12
B11
B14
B15
B13
E0
E1
F0
F1
G0
G1
H0
H1
A0
MAPPING
v0 (EW8)
Tail elements get CORRUPTED
They were shuffled as EW16, but we lost that information
A1
B0
B1
C0
C1
D0
D1

## Slide 152: Reshuffle (undisturbed policy)
A0
A1
E0
E1
B0
B1
F0
F1
G0
G1
C0
C1
D0
D1
H0
H1
V0 mapping: EW16
vld, ew16
L0
L1
L2
t
L3
vld, ew8
New data-width in the destination and tail elements exposed?
  Reshuffle destination with new encoding!
  Byte mapping is preserved!

## Slide 153: Reshuffle (undisturbed policy)
New data-width in the destination and tail elements exposed?
  Reshuffle destination with new encoding!
  Byte mapping is preserved!
Reshuffle injected when needed
A0
A1
E0
E1
B0
B1
F0
F1
G0
G1
C0
C1
D0
D1
H0
H1
A0
A1
E0
E1
B0
B1
F0
F1
G0
G1
C0
C1
D0
D1
H0
H1
V0 mapping: EW16
V0 mapping: EW8
vld, ew16
vld, ew8
reshuffle
L0
L1
L2
t
L0
L1
L2
L3
L3

## Slide 154: Reshuffle (undisturbed policy)
A0
A1
E0
E1
B0
B1
F0
F1
G0
G1
C0
C1
D0
D1
H0
H1
A0
A1
E0
E1
B0
B1
F0
F1
G0
G1
C0
C1
D0
D1
H0
H1
V0 mapping: EW16
V0 mapping: EW8
V0 mapping: EW8
vld, ew16
vld, ew8
vld, ew8
reshuffle
L0
L1
L2
t
L0
L1
L2
L3
L3
A0
A1
E0
E1
B0
B1
F0
F1
G0
G1
C0
C1
D0
D1
H0
H1
L0
L1
L2
L3
New data-width in the destination and tail elements exposed?
  Reshuffle destination with new encoding!
  Byte mapping is preserved!
Reshuffle injected when needed

## Slide 155: Scalar Core + Caches effect on performance
Replace CVA6 with ideal dispatcher
  FIFO with V instructions
  Ideal issue rate
  Narrow lines on plot

## Slide 156: Scalar Core + Caches effect on performance
Scalar Core + Caches effect on performance
Replace CVA6 with ideal dispatcher
  FIFO with V instructions
  Ideal issue rate
  Narrow lines on plot
Show CVA6 + $ non-idealities

## Slide 157: Scalar Core + Caches effect on performance
Replace CVA6 with ideal dispatcher
  FIFO with V instructions
  Ideal issue rate
  Narrow lines on plot
Show CVA6 + $ non-idealities
Show VU1.0 non-idealities

## Slide 158: Reduction performance
dotp benchmark (chained vmul, vredsum)
  Varying vector length in Byte

## Slide 159: Reduction performance
dotp benchmark (chained vmul, vredsum)
  Varying vector length in Byte
Longer vectors == Higher Efficiency!!
Performance:
26% on ideal
Performance:
94% on ideal

## Slide 160: Reduction performance
dotp benchmark (chained vmul, vredsum)
  Varying vector length in Byte
  Varying vector element size: 8-bit / 64-bit
Cycle count almost independent on element size
8-bit elements == ~8x the throughput of 64-bit elements
4096 8-bit Elements 512 64-bit Elements

## Slide 161: Reduction performance
dotp benchmark (chained vmul, vredsum)
  Varying vector length in Byte
  Varying vector element size: 8-bit / 64-bit
  Varying number of lanes
High overhead by inter-lanes reduction phase
for shorter vectors or more lanes

## Slide 162: Reduction performance
dotp benchmark (chained vmul, vredsum)
  Varying vector length in Byte
  Varying vector element size: 8-bit / 64-bit
  Varying number of lanes
High overhead by inter-lanes reduction phase
for shorter vectors or more lanes

## Slide 163: Barber's Pole layout
M. Cavalcante et. Al, "Ara: A 1 GHz+ Scalable and Energy-Efficient RISC-V Vector Processor with Multi-Precision Floating Point Support in 22 nm FD-SOI"
Ara RVV 0.5
Barber's Pole layout to speed up operand fetch
Ara RVV 1.0
No Barber's Pole
e.g., on matmul
Small positive effect on short/medium vectors
  No bank conflicts upon first operands fetch
Small negative effect on medium/long vectors
  More bank conflicts on different instructions

## Slide 164: Multi-core performance, throughput, efficiency
System with 16 FPUs
Example: 8C2L = 8 (Ara+CVA6) instances